## Slide 1
October 2024
Designe and implement a small office network
Presented by Amr A. Fahmy
Abdelrahman R. kotb
Abdullah M. Shehata
Omar M. Hassan

## Slide 2
Throughout our learning journey in the networking field, we have observed that a significant number of job opportunities for junior network engineers are centered around the implementation and design of office networks for startup companies. These roles provide an excellent opportunity for us to further develop and refine our skills in real-world environments.
We will delve into the technical aspects and specific details of the project at a later stage.
Origin of the idea
October 2024
01

## Slide 3
02
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Problem
A company with two branches is facing challenges in implementing a Local Area Network (LAN) for each branch. Each branch requires segmentation into multiple VLANs to efficiently manage network traffic and enhance security. Additionally, the company aims to activate the DHCP protocol on the LAN routers to dynamically assign IP addresses to devices within each branch.
Moreover, the company needs to establish a connection between the two branches as well as provide internet access. This would involve configuring the appropriate routing protocols and ensuring secure and reliable communication between the branches and the external network.

## Slide 4
Solution steps
Thynk Unlimited
Presentation 2024
-
03
Network topology
Switches configuration
& VLANs
routers configration & DHCP
01
02
03

## Slide 5
Topology
04
-
-

## Slide 6
We began by accessing the switch’s Command Line Interface (CLI) and entering configuration mode to initiate the setup process. Once in configuration mode, we navigated to the specific switch ports and proceeded to assign each port to the appropriate VLANs that we had previously created. This step was essential for logically segmenting the network and ensuring that each VLAN could operate independently, aligning with the network design and security requirements.
Configuration on switch
05

## Slide 7
We write a configuration for DHCP pools on a network router. Each DHCP pool defines a set of IP addresses that will be dynamically assigned to devices within specific VLANs or subnets. In this configuration, there are three distinct DHCP pools: "cisco," "HR," and "IT." Each pool specifies a unique network address range, subnet mask, default gateway (or router), and DNS server. For instance, the "cisco" pool is configured for the 192.168.1.0/24 network, with a default router of 192.168.1.1 and a DNS server of 8.8.8.8.
The "HR" and "IT" pools are configured similarly, each with their respective network ranges: 192.168.4.0/24 for HR and 192.168.5.0/24 for IT. Both pools also point to the same DNS server (8.8.8.8), with default routers specific to their network ranges—192.168.4.1 for HR and 192.168.5.1 for IT. These settings ensure that devices within each VLAN are assigned appropriate IP addresses, gateways, and DNS information for network connectivity and communication.
06
Configuration on router

## Slide 8
cont.
The image shows the configuration of network interfaces on a Cisco router. The router’s GigabitEthernet0/0 interface is assigned the IP address 192.168.1.1 with a subnet mask of 255.255.255.0, indicating that it is part of the 192.168.1.0/24 network. The duplex and speed settings are set to auto, meaning the router will automatically negotiate the best settings with connected devices. There is also a "no IP address" command under GigabitEthernet0/0.1, indicating that no IP address is assigned to this subinterface.
The configuration also defines two subinterfaces: GigabitEthernet0/0.4 and GigabitEthernet0/0.5. These subinterfaces are used to manage VLAN traffic, as indicated by the encapsulation dot1Q command, which specifies the VLAN IDs 20 and 10, respectively. The subinterfaces are assigned IP addresses (192.168.4.1 and 192.168.5.1) with appropriate subnet masks to support VLAN 20 and VLAN 10. Finally, the GigabitEthernet0/1 interface is configured with no IP address, set to duplex and speed auto, and marked as shutdown, meaning it is currently disabled.
Configuration on router
07

## Slide 9
Configuration on router
cont.
08
a configuration of serial and VLAN interfaces on a router. The Serial0/0/0 interface is assigned the IP address 192.168.7.1 with a subnet mask of 255.255.255.0, and a clock rate of 2000000 is set, indicating this is likely part of a point-to-point WAN connection. The Serial0/0/1 interface is not assigned an IP address and is marked as shutdown, meaning it is disabled and not in use, but its clock rate is still configured at 2000000.
Additionally, there are three VLAN interfaces: Vlan1, Vlan10, and Vlan20. None of these VLAN interfaces have IP addresses, but each is associated with a unique MAC address, which allows them to handle traffic for specific VLANs. The configuration also includes a static route using the ip route command, routing traffic from the 192.168.6.0/24 network to the 192.168.7.2 next hop. The ip flow-export version 9 command is present, indicating that NetFlow is enabled on the router to monitor and export traffic data for network analysis.

## Slide 10
Conclusion
In summary, we successfully designed and implemented a comprehensive office network project. The DHCP was activated on the router to dynamically allocate IP addresses, and VLANs were meticulously configured on the switch to ensure efficient network segmentation. Additionally, this branch was seamlessly connected to another branch, mirroring the same configurations. This inter-branch connectivity was achieved through a reliable Internet Service Provider, ensuring robust and continuous network communication.
10

## Slide 11
The project
https://drive.google.com/file/d/1da-QRX-KBZWew4RpBSlZTJvS87ynAc7j/view?usp=sharing

## Slide 12
Thank You